## Slide 1: Vulnerability Map for Ogallala Aquifer
For Fluoride Contamination using Machine Learning
Group Members:
Kushum K C
Rakshya Shrestha
Zaki Ahmed Choudhary

## Slide 2: Introduction
Contaminant (4)
Fluoride is top pollutant that contaminates the natural water resources in NW Texas.
Ample data available for the Fluoride concentration in the wells on Ogallala aquifer
It’s a surficial pollutant
Ogallala Aquifer (4)
Lies at Northwest Texas
one of the major aquifer and part of high plains aquifer system
shallow water table.
water used for agricultural purpose (irrigation) is at high risk of overextraction

## Slide 3: Sources of Fluoride
Dosing of municipal water with fluoride salts for skeletal health
Fluoride used in healthcare products
Dissolution of fluoride bearing rocks by groundwater
Cutoff for Fluoride Concentration
The World Health Organization recommends an MCL of 1.5 mg/L and it is reasonable to anticipate the EPA lowering their MCL to a similar level in the near future (2006) (3)
Benefits and Hazards of Fluoride in drinking water
Low concentration of Fluoride in water is beneficial (for teeth and bone)
Prolonged exposure to high concentration causes health hazards
  dental fluorosis (pitting of teeth)
  skeletal fluorosis
  Hinders brain development of children

## Slide 4: Data Compilation and Filtering
Data Compilation
PRISM Data – 30 years normal
Precipitation, Elevation, Temperature
TWDB (Texas Water Development Board)
Major Aquifer (Ogallala) Water Quality Data
Well Main Data
SSURGO data
Soil Parameter
Data Filtering
PRISM Data : 1991 to 2020
TWDB data
    Temporal: >2000
    Spatial: Ogallala Aquifer
    Parameter: Fluoride Concentration, (Averaged for each well)

## Slide 5: Soil Parameters Extraction
SSURGO Data
Soil Texture Map using QGIS
Soil Texture Map using Python

## Slide 6: Data Description
SN | Name | Description | Data Type | Units
1 | StateWellID | Well ID number | Integer | 
2 | Latitude | Latitude | Double | Decimal Degree
3 | Longitude | Longitude | Double | Decimal Degree
4 | Fluoride_avg | Fluoride contamination | float | mg/l
5 | WellDepth | depth of well | float | feet
6 | Rainfall | precipitation (30- year normal 1991-2020) | float | inch
7 | Elevation | Elevation (Resolution 4 km) | float | feet
8 | Tmin | minimum temperature (30- year normal 1991-2020) | float | °F
9 | Tmax | maximum temperature (30- year normal 1991-2020) | float | °F
10 | Tmean | mean temperature (30- year normal 1991-2020) | float | °F
11 | claytotal_l | Mineral particles less than 0.002mm in equivalent diameter as a weight percentage of the less than 2.0mm fraction for low level | Float | %
12 | claytotal_r | Mineral particles less than 0.002mm in equivalent diameter as a weight percentage of the less than 2.0mm fraction for RV level | Float | %
13 | claytotal_h | Mineral particles less than 0.002mm in equivalent diameter as a weight percentage of the less than 2.0mm fraction for high level | Float | %
14 | ksat_l | The amount of water that would move vertically through a unit area of saturated soil in unit time under unit hydraulic gradient in low level | Float | %
15 | ksat_r | The amount of water that would move vertically through a unit area of saturated soil in unit time under unit hydraulic gradient RV level | Float | %
16 | ksat_h | The amount of water that would move vertically through a unit area of saturated soil in unit time under unit hydraulic gradient low level | Float | %
17 | awc_l | The amount of water that an increment of soil depth, inclusive of fragments, can store that is available to plants for low level | Float | %
18 | awc_r | The amount of water that an increment of soil depth, inclusive of fragments, can store that is available to plants for RV level | Float | %
19 | awc_h | The amount of water that an increment of soil depth, inclusive of fragments, can store that is available to plants for high level | Float | %
20 | pi_l | The numerical difference between the liquid limit and plastic limit for low level | float | %
21 | pi_r | The numerical difference between the liquid limit and plastic limit for RV level | float | %
22 | pi_h | The numerical difference between the liquid limit and plastic limit for high level | float | %
23 | ph_l | The negative logarithm to the base 10, of the hydrogen ion activity in the soil in low level | Logarithmic unit | 
24 | ph_r | The negative logarithm to the base 10, of the hydrogen ion activity in the soil in RV level | Logarithmic unit | 
25 | ph_h | The negative logarithm to the base 10, of the hydrogen ion activity in the soil in high level | Logarithmic unit | 

## Slide 7: Variables Selection
Selection Criteria for X Variables
Correlation between Variables
  Kendall density function:- calculates Kendall rank correlation coefficient (-1,1), 0 indicates no correlation.
Feature Importance
  Using Decision Tree
  Using Random Forest
Y Variable
Pollutant (Fluoride Concentration exceedance Indicator)

## Slide 8: Feature selection based on importance
Random Forest (left) and CART method (right)

## Slide 9: Variables and Logistic Regression (model 1)
Logistic Regression
classifies the data into a binary dataset (0,1)
Training and testing dataset (70:30)
Model fit using logistic regression
Hyperparameter: -
  C = 10**9
  where c is regularization strength. for high C value, model fits the training dataset as closely as possible.
Variables for Model 1
Well Depth
Rainfall
Elevation
awc_low
Temperature (minimum)
pi_representative
ph_representative
Claytotal_representative
from sklearn.linear_model import LogisticRegression

## Slide 10: Model 1 Logistic Regression Training Data
Accuracy | 0.793
Precision | 0.783
Recall | 0.994

## Slide 11: Model 1 Logistic Regression Testing Data
Accuracy | 0.817
Precision | 0.811
Recall | 0.986

## Slide 12: Naïve Bayes Classification (NBC)
Probabilistic method of variable classification
  Calculates the PDF for each predictor variables given its bias (mean)and Variance (standard deviation)
Modified using the Gaussian distribution (Gaussian Naïve Bayes)
  Continuous Dataset
Assumption:
Y variables are Conditionally Independent given the Input Variables (X), which is not always true.
Features are independent of each other given the class label
Library in Python
from sklearn.naive_bayes import GaussianNB

## Slide 13: Model 1 Naïve Bayes Training Data
Accuracy | 0.788
Precision | 0.838
Recall | 0.883

## Slide 14: Model 1 Naïve Bayes Testing Data
Accuracy | 0.772
Precision | 0.853
Recall | 0.841

## Slide 15: Model 2: Logistic Regression
947 wells
Parameters selection:
Well Depth
Elevation
Rainfall
Minimum temperature
Soil clay content
Average water content of soil
Soil plasticity
Soil pH.
Exceedance: greater than 1.5 ppm
Training dataset: 70%

## Slide 16: Results: Model 2 LR
Accuracy: 0.786
Precision: 0.782
Recall: 0.976

## Slide 17: Model 3 : Feature selection
Feature importance

## Slide 18: X Variables
Well depth
Rainfall
Elevation
Available water Content
Plasticity Index (pi_r)
pH_r

## Slide 19: Model 3 Logistic Regression Training Data
Accuracy | 0.793
Precision | 0.782
Recall | 0.995

## Slide 20: Model 3 Logistic Regression Testing Data
Accuracy | 0.817
Precision | 0.811
Recall | 0.986

## Slide 21: Model 3 Naïve Bayes Training Data
Accuracy | 0.797
Precision | 0.818
Recall | 0.932

## Slide 22: Model 3 Naïve Bayes Testing Data
Accuracy | 0.779
Precision | 0.787
Recall | 0.967

## Slide 23: K-Nearest Neighbor (KNN)
Memorization learning algorithm also known as Lazy learner
KNN regression is used for Continuous variables
Hyperparameters in KNN
Value of K (number of neighbors to be considered)
Weight = distance (Haversine distance)
In Python:
from sklearn.neighbors import KNeighborsRegressor
Assumptions in KNN
Similar items are closer to each other than the dissimilar items

## Slide 24: Fitting KNN Models
For Testing dataset
KNN with LR Probabilities
KNN with Naïve Bayes Probabilities

## Slide 25: Prediction across entire domain of Ogallala Aquifer
Coordinates of the Ogallala Aquifer Extents extracted from QGIS.
  Lat min = 31.7434151337257013 , Lat max = 36.5012320286370979
  Lon min = -103.0647347331729975, Lon max = -100.0000629878099971
Mesh of all the possible points between minimum and maximum on both axis.
  Step Size = 0.1 Decimal Degrees (11.1km)
KNN Predictions for the mesh of latitudes and longitudes using both models.

## Slide 26: Integrating LR Model and Naïve Bayes Model
During Fitting and testing process of the LR and Naïve Bayes model independently,
Naïve Bayes Classifier model performed slightly better than the Logistic regression model in terms of Accuracy and Precision.
While fitting the KNN models using the probabilities of pollutant prediction from LR and Naïve Bayes modes,
Observed Vs Predicted plot for probability from LR aligns more closely to the X=Y line.
Considering that the errors associated with each model are independent of each other, we decided to give equal weightage to both model with an aim to minimize the error compiling the both models.

## Slide 27: Vulnerability Map
Equal Weightage for KNN LR and KNN NBC.

## Slide 28: Conclusion
Southern part is more susceptible to Fluoride contamination.
TWDB data and SSURGO data can be used to predict the vulnerability map for the aquifer and KNN model can be used to prepare a grided dataset.
Logistic Regression model gave better model fit while modelling with same variables than Naïve Bayes.

## Slide 29: References:
Full GWDB | https://www.twdb.texas.gov/groundwater/data/gwdbrpt.asp
Soil SSURGO Data | https://data.nal.usda.gov/dataset/united-states-general-soil-map-statsgo2
Prism Data (precipitation, Elevation and Temperature) | https://prism.oregonstate.edu/normals/
Ogallala Boundary Map | https://www.twdb.texas.gov/mapping/gisdata.asp
Data:

## Slide 30: References:
Literature Review:
1 | Madani, A., M. Hagage, and S.F. Elbeih, Random Forest and Logistic Regression algorithms for prediction of groundwater contamination using ammonia concentration. Arabian Journal of Geosciences, 2022. 15(20): p. 1619.
2 | Uddameri, V., A.L.B. Silva, S. Singaraju, G. Mohammadi, and E.A. Hernandez, Tree-based modeling methods to predict nitrate exceedances in the Ogallala aquifer in Texas. Water, 2020. 12(4): p. 1023.
3 | https://www.caee.utexas.edu/prof/maidment/giswr2013/Reports/Stehouwer.pdf
4 | https://www.twdb.texas.gov/publications/reports/numbered_reports/doc/R380_AquifersofTexas.pdf

## Slide 31: THANK YOU